## clearing and grubbing

(REV 09-16-09) (01-13)

ARTICLE 110-2 (Pages 149 and 150) is expanded by the following new Subarticle:

110-2.5 Clearing and Grubbing Locations. Locations to be cleared and grubbed will be described in a work document or plans.

Remove portions of fence when necessary to gain access within fenced areas. Restore fence immediately following completion of work described in the work document.  Cost of restoring the fence will be included in the cost of clearing and grubbing.

Report, before beginning work, all damaged fence, fence posts and other appurtenances such as sign posts and bases, delineator posts, guardrail or barrier walls, light poles, endwalls, pipes, drainage structures, poles, guys, landscape areas, etc., to the Engineer.  Damaged fence, fence post or other appurtenance found after beginning work will be deemed damaged and will be replaced at no cost to the Department.

SUBARTICLE 110-9.1 (Page 153). The last sentence is deleted and the following substituted:

No disposal of debris will be allowed into waterways.

ARTICLE 110-9 (Pages 153 and 154) is expanded by the following new subarticle:

110-9.6 Stockpiling Debris:  Stockpile outside of the clear zone or remove and dispose from the right-of-way all material that was the result of the clearing and grubbing operation at the end of each day.  Provide disposal areas approved by the Engineer, in accordance with the applicable requirements of state and local laws, ordinances, or regulations.

SUBARTICLE 110-11.1 (Page 155) is expanded by the following:

When areas of clearing & grubbing are designated to be paid for separately by the acre, the quantity to be paid for will be determined by measurement of the areas authorized by the Engineer to be cleared & grubbed and acceptably completed. Measurements of the above areas will be rounded to the nearest one thousandths (0.001) acre.